## Slide 1
Real-Time Anomaly Detection in ICS/OT using Behavioral EDR
A Multi-Layered Statistical Defense for Critical Infrastructure
PRESENTED BY
Safna S
DOMAIN
Cyber Security
GUIDED BY
Rahul R, Assistant Profess

## Slide 2
The Critical Need for ICS/OT-Specific Security
Continuous Data Streams
■ ICS data consists of continuous sensor measurements (flow, pressure, level), not discrete files or network packets.
Physical Consequences
■ A breach in OT can lead to physical damage, environmental hazards, and direct threats to public safety.
Subtle Attack Vectors
■ Attacks often manifest as subtle sensor drifts that stay within "acceptable" ranges but violate process logic.
The Signature Gap
■ Conventional tools cannot detect zero-day attacks that have no pre-existing signatures or documented patterns.

## Slide 3
Introducing Behavioral EDR for ICS
Behavioral Analysis
■ Learns the unique statistical fingerprint of normal plant operations to establish a trustworthy reference.
Endpoint Detection
■ Monitors process-level variables directly at the sensor/actuator interface for maximum visibility.
Multi-Layered Pipeline
■ Integrates 12 specialized mathematical formulas—from **EWMA** to **Shannon Entropy**—for comprehensive coverage.
Frozen Baseline
■ A key innovation that locks model parameters after warmup to prevent adversarial drift and model poisoning.

## Slide 4
The 12-Formula Detection Engine
1. State Vector Extraction
■
Consolidates 14 sensors into a real-time snapshot.
X_t = [x₁(t), x₂(t), ..., x₁₄(t)]ᵀ
2. Sliding Window
■
Maintains the 50 most recent states for context.
W_t = {X_{t-n+1}, ..., X_t}
3. EWMA Mean & Variance
■
Computes smoothed baselines resistant to noise.
μ_t = α·X_t + (1-α)·μ_{t-1}
4. Mahalanobis Distance
■
Measures multivariate deviation with correlations.
D_M(t) = √((X_t-μ)ᵀ·Σ⁻¹·(X_t-μ))
5. Probability & Reconstruction
■
Maps distance to likelihood and raw error metrics.
P(X_t) = exp(-0.5·(D_M/10)²)
6. Entropy & Timing
■
Detects disorder and communication irregularities.
H = -Σ P(sᵢ)·log(P(sᵢ))
7. Risk & Unknown Scores
■
Aggregates signals to identify zero-day threats.
U_t = w₁·(1-P) + w₂·E_t + w₃·T + w₄·H
8. Persistence Check
■
Filters transient noise for high-confidence alerts.
Persistent = (Σ last_5_scores) > γ

## Slide 5
The "Frozen Baseline" Strategy
Warmup Phase
■ The system learns the plant's normal behavior during the first 200 samples. ■ Establishes initial statistical parameters in a clean environment.
Parameter Lock
■ At sample 200, the mean (μ), variance (σ²), and inverse covariance (Σ⁻¹) are permanently frozen. ■ Reference point is secured.
Drift Prevention
■ Attacks cannot "poison" the model by gradually shifting the reference point over time. ■ Ensures long-term reliability of detection.

## Slide 6
Core Metric: Mahalanobis Distance (D_M)
NORMAL BASELINE (AVG)
4.21
ATTACK DEVIATION (AVG)
177.41
42× Separation
Ratio between normal and attack data points
Beyond Euclidean Distance
■ Accounts for the covariance structure between sensors, detecting coordinated anomalies that single-sensor monitoring misses.
Optimal Threshold Strategy
■ A threshold of **D_M > 5** provides the optimal balance between high recall and operational continuity (97.6% Precision).
Clear Distinction
■ The massive statistical gap ensures that genuine cyber attacks are clearly distinguishable from normal operational noise.

## Slide 7
Detecting the Unknown: The U
t
Score
Unknown Behavior Score
U
t
= w
1
(1-P) + w
2
E
t
+
w
3
T
s
+ w
4
H
A weighted aggregation of inverse probability, reconstruction error, timing deviation, and Shannon entropy.
Identifying Zero-Day Attacks
■ Flags behavior that has never been seen during the training phase, enabling detection of novel threats without signatures.
Proactive Defense
■ Does not require prior knowledge of an attack's characteristics, methods, or specific industrial protocol vulnerabilities.
Actionable Intelligence
■
High U
t
scores trigger immediate forensic investigation, providing
operators with a clear signal of abnormal process evolution.

## Slide 8
Validation: The SWaT Testbed
1.4M
TOTAL RECORDS
51
SENSORS & ACTUATORS
41
ATTACK SCENARIOS
Source & Infrastructure
■ Developed by iTrust, SUTD (Singapore). A fully operational water treatment facility with 6 interconnected sub-processes.
Realistic Attack Data
■ Dataset covers 11 days of operation, including coordinated red-team attacks like valve manipulation and sensor spoofing.
Ground Truth Validation
■ Rigorous validation against 41 different cyber-physical attack scenarios to ensure comprehensive detection coverage.

## Slide 9
Performance Benchmarking: Superior Results
F1-Score Comparison (SWaT Dataset)
Precision
97.6%
■ Extremely low false alarm rate; critical for maintaining trust in industrial operations.
F1-Score
93.3%
■ Best-in-class balanced performance, outperforming deep learning methods.
Accuracy
89.4%
■ Reliable detection across diverse and sophisticated cyber-physical attack vectors.

## Slide 10
The Behavioral EDR Dashboard
Real-Time Monitoring
■ Live Metric Tracking
Continuous visualization of
Mahalanobis Distance (D_M), Unknown
Score (Ut), and Shannon Entropy.
Visual Intelligence
■ System Health Gauge
Instant visual status of the monitored
industrial process with a rolling 100-
packet threat level.
SOC Alert Table
■ Detailed Attribution
Filterable alert logs with specific sensor
identification and severity-based drill-
down panels.
Interpretability
■ Transparent Evidence
Moves beyond "black-box" AI—
operators see the exact mathematical
formulas behind every detection.
Event Timeline
■ Attack Narrative
Chronological history of detected
anomalies, system responses, and
forensic audit trails.
Simulation Control
■ Interactive Testing
Play/pause/reset controls with speed
adjustment to observe model response
to diverse scenarios.

## Slide 11
Conclusion & Future Roadmap
Project Summary
■ Successfully delivered a deployable, real-time, and highly interpretable EDR system specifically tailored for the unique constraints of ICS/OT environments.
Key Accomplishment
■ Outperformed standard ML models with a **93.3% F1-score** while maintaining full transparency through a 12-formula statistical pipeline.
Future Scope
■ **Multi-Plant Monitoring**: Centralized visibility across global industrial fleets.
■ **Deep Learning Ensemble**: Combining statistical rigor with neural pattern recognition.
■ **Automated Response**: Direct integration with PLC safety routines for instant mitigation.
■ **Protocol Analysis**: Adding support for Modbus and DNP3 packet-level inspection.

## Slide 12
Thank You